## Slide 1: Throwing Balls and other stuff
David Giandomenico December 13, 2014

## Slide 2: Talk Overview
Projectile Trajectory
Momentum transfer
  Linear Momentum
  Angular Momentum
    Moments of inertia
Grip forces
Kinetic energy of rotating parts
Physics
Math
More Physics

## Slide 3: FIRST Games with Shooting
 2014: Aerial Assist – Shoot 2ft / 3lb exercise balls
 2013: Ultimate Ascent – Launch Frisbee®s
 2012: Rebound Rumble – Shoot solid foam balls
☐ 2011: Logomotion – Handle inflatable shapes
 2010: Breakaway – Kick soccer balls
 2009: Lunacy – Shoot “orbit” balls
 2008: FIRST Overdrive – Lift or shoot large exercise balls
☐ 2007: Rack 'n Roll – Handle inflatable rings; Lift robots
 2006: Aim High – Shoot solid foam balls
☐ 2005: Triple Play – Move large tetrahedrons
☐ 2004: FIRST Frenzy: Raising the Bar – Move medium & large balls

## Slide 4: Types of Launchers
Energy Transfer
  Example: Release of a spring like a catapult
Momentum Transfer
  Example: Bat & ball, or Flywheel tennis ball launcher
Constant Force Transfer
  Example: Constant friction drive wheel
Notes: If you don’t know, you may not be able to characterize your launcher, to solve inconsistent shooting problems.

## Slide 5: Find the Requirements
Projectile
  Kinematics – motion of the object
  Launch energy of Projectile
Machine
  Momentum & energy transfer
  Energy losses during launch
  Total input energy required

## Slide 6: Specify the Target Trajectory
Chart: Launch Trajectory
| 0.0 | 0.555758918060194 | 1.111517836120388 | 1.667276754180582 | 2.223035672240776 | 2.77879459030097 | 3.334553508361164 | 3.890312426421358 | 4.446071344481551 | 5.001830262541746 | 5.55758918060194 | 6.113348098662132 | 6.669107016722327 | 7.224865934782521 | 7.780624852842715 | 8.33638377090291 | 8.892142688963104 | 9.447901607023297 | 10.0036605250835 | 10.5594194431437 | 11.11517836120388
Center of Ball | 2.5 | 3.6579 | 4.6924 | 5.6037 | 6.3918 | 7.0565 | 7.598 | 8.0162 | 8.3111 | 8.4827 | 8.5311 | 8.4561 | 8.2579 | 7.9364 | 7.4917 | 6.9236 | 6.2323 | 5.4177 | 4.4798 | 3.4187 | 2.2342
Top of Ball | 3.5652 | 4.7231 | 5.7577 | 6.669 | 7.457 | 8.1217 | 8.6632 | 9.0814 | 9.3763 | 9.5479 | 9.5963 | 9.5213 | 9.3231 | 9.0016 | 8.5569 | 7.9888 | 7.2975 | 6.4829 | 5.545 | 4.4839 | 3.2994
Bottom of Ball | 1.4348 | 2.5927 | 3.6272 | 4.5385 | 5.3266 | 5.9913 | 6.5328 | 6.951 | 7.2459 | 7.4175 | 7.4658 | 7.3909 | 7.1927 | 6.8712 | 6.4265 | 5.8584 | 5.1671 | 4.3525 | 3.4146 | 2.3534 | 1.169
top of goal | 9.9792 | 12.9792
bot of goal | 0 | 6.8958
5' Robot
tolerance
Truss | 6.8958 | 6.8958

## Slide 7: Verify the trajectory is parabolic
Notes: In many competitions, there is concern that “windage” may influence the trajectory.

## Slide 8: Track trajectory using Kinovea
Open source software freely available at: http://www.kinovea.org/
Notes: Using free software “Kinovea”, you can see the trajectory. At an early stage of the competition, the trajectory can be verified, even without a robot.

## Slide 9: Trajectory is Parabolic ✓
–– Measured
–– Desired
–– Parabolic fit (quadratic)
Observed vs Measured Trajectory

## Slide 10: Game Requirement ( an example )
Solid foam ball
Mass: 0.5 Kg ( a little more than 1 lb )
Height to target: 2m ( a little more than 6ft)
Distance to target: 3m minimum
Target is vertical on wall

## Slide 11: Kinematics

## Slide 12: Find Launch Velocity V and Angle

## Slide 13: Find Launch Velocity V and Angle

## Slide 14: Find Launch velocity V and angle

## Slide 15: Find Launch velocity V and angle
Divide:

## Slide 16: Launch Velocity: Example Calculation

## Slide 17: Kinetic Energy ( Translational ) Example Calculation
Revisit this later to add rotational energy...

## Slide 18: Power Limitations
Estimate: If our motor system can deliver 150W with 100% efficiency, how long will it take, and how far will our projectile travel as we accelerate constantly from 0 to our target V?
assume constant acceleration†
Our Example:
†Acceleration will not be constant, but this is still close enough.
Notes: Constant acceleration is not consistent with constant power, but this estimate still serves to illustrate the point.
More carefully, d = (2/3) V t, since the speed rises faster than linear, but Force is infinite at t=0 for constant power.

## Slide 19: Power Limitation - Conclusion
Launch mechanism will probably not fit in our robot.
Instead release stored energy over a short time.
†Acceleration will not be constant, but this is still close enough.
Notes: Constant acceleration is not consistent with constant power, but this estimate still serves to illustrate the point.
More carefully, d = (2/3) V t, since the speed rises faster than linear, but Force is infinite at t=0 for constant power.

## Slide 20: Which of These Things Doesn’t Belong?
(A)
(B)
(C)
(D)
(E)

## Slide 21
Jessica. 29 MPH float serve in slow motion. California Heat Volleyball Club Uploaded by: GenjitsuDojo
Notes: Add video

## Slide 22
Golf impact – Slow Motion Video Uploaded by: BiomechanicsMMU
Notes: Add video

## Slide 23
Tim Linecum pitching in slow motion – Red Bull Moments Uploaded by: redbull
Notes: Add video

## Slide 24
Barry Harper batting form –slow motion
Uploaded by: Gus M
Notes: Add video

## Slide 25: Another phenomenon…

## Slide 26
(A)
(B)
(C)
(D)
(E)
Which of These Things Doesn’t Belong?

## Slide 27
Pitching requires all energy to be delivered in “real time”
All of the other methods use stored energy released in a short duration impact.
Which of These Things Doesn’t Belong?

## Slide 28: The Catapult
What sources of energy loss do we expect?
2014 Funk Cannon, FIRST 846

## Slide 29: Energy Losses in a Catapult

## Slide 30: Energy Losses in a Catapult
Observed Losses:
Residual energy in arm
Deformation of projectile
Transfer of energy to robot frame
2014 Funk Cannon, FIRST 846

## Slide 31: Ball Drop Loss & Efficiency
Initial Energy:
Final Energy:
Drop Efficiency:
hi
hf
Notes: Video tape drop with scale on wall. Measure bottom of ball. Try at different heights to confirm energy efficiency is consistent.

## Slide 32: Computing the Required Energy for a Catapult Spring
Determining Required Energy
Compute ball’s energy from trajectory
Divide by “ball drop efficiency” to get the launch energy
Add residual energy of arm Use CAD to compute IArm, or do estimate manually.
Add energy imparted to robot frame Did not consider in design, except to make all wheels on ground.; May be hard...
2014 Funk Cannon, FIRST 846
Best guess. This is clearly wrong if efficiency is small.
Notes: If efficiency is low, computing the launch energy will be wrong. More thought is needed in this case on how to estimate the loss. –dg.

## Slide 33: The Kicker
2010 BreakAway
Ball must remain outside robot.

## Slide 34: Kicker – Compute Energies
Calculate trajectory and launch energy
Estimate impact energy loss ( bounce test)
Solve energy / momentum equations
  Consider choosing the mass of hammer to equal the ball’s mass. (more on this later...) See: Newton’s Cradle

## Slide 35: The Kicker
Transfer of Energy from Spring to Hammer
...for a Torsion Spring
Stored energy:
Kinetic energy:
Notes: We model trajectory as in first case. Let’s consider energy in hammer first, then consider impact. The force profile of the spring does not matter.

## Slide 36: Linear to Angular
...for a Torsion Spring
Linear energy:
Hammer’s momentum may be modeled as Angular momentum
Notes: This will allow us to add in other masses in the system, like the Hammer’s handle.

## Slide 37: Linear to Angular
...for a Torsion Spring
Now we can include the effects of the hammer’s arm
Notes: This will allow us to add in other masses in the system, like the Hammer’s handle.

## Slide 38: Linear to Angular
...for a Torsion Spring
Equating the spring energy to the hammer’s kinetic energy:
Since:
Notes: This will allow us to add in other masses in the system, like the Hammer’s handle.

## Slide 39: Angular back to Linear
...for a Torsion Spring
And we can bring this all back to the linear system...
From before
Linear momentum, p
Notes: This will allow us to add in other masses in the system, like the Hammer’s handle.

## Slide 40: Kicker – The Collision
We Know:
Energy required for ball trajectory
Hammer speed & Momentum as a function of Spring Energy
We need:
Energy & Momentum transfer at time of Kick

## Slide 41: Angular – Linear Parallels
...for a Torsion Spring
From before
Linear momentum, p
Notes: This will allow us to add in other masses in the system, like the Hammer’s handle.

## Slide 42: Newton’s Law (paraphrased)
1) ....an object either is at rest or moves at a constant velocity, unless acted upon by an external force.
2) F = ma (acceleration is proportional to force, and inversely proportional to mass)
3) When one body exerts a force on a second body, the second body simultaneously exerts a force equal in magnitude and opposite in direction to that of the first body.
From (2) and (3) we can show conservation of momentum.

## Slide 43: Conservation of Momentum
(2)
A
B
(3)
For any interval Δt,

## Slide 44: Conservation of Momentum
A
B
A
B
A
B
During collision, momentum is added to B and removed from A.

## Slide 45: Conservation of Energy vs Conservation of Momentum
Total energy is conserved in the isolated system, but kinetic energy is not.
Momentum:
Kinetic Energy:
For conservation of Total Energy,
we must account for the energy absorbed during the impact (if any).
Total Energy:
Notes: Which is conserved?

## Slide 46: Extreme case: Elastic Collision
Momentum:
Energy:
Rearrange:
(3)
(4)
Introduce α:
(1)
(2)
(2)
Divide (3) by (4):
(5)
set (4)=(5)

## Slide 47: Newton’s Cradle – Elastic Collisions
http://onlyhdwallpapers.com

## Slide 48: Extreme case: Completely Inelastic Collision
Momentum:
Completely Inelastic:
Introduce α:
(1)
(2)
www.chegg.com
Substitute:
Ballistic test to measure bullet speed

## Slide 49: Kicker – conclusion for elastic case
We can bound the collision between Elastic and Inelastic cases.
If the ball we are kicking has a high return bounce, we can model the collision as elastic with reasonable confidence.
In this case, choosing the equivalent mass of the kicker to equal the mass of the ball will stop the kicker on impact. This will result in a minimum of wasted energy.
Then we can simply determine the required spring energy as the ball energy / efficiency from the bounce test.
With a working machine, the kicker-ball collision can be better analyzed, and the design may be iterated.
Notes: This is inconsistent, since if we don’t have 100% efficient bounce test, then we can’t have a 100% elastic collision. If the result is not satisfactory, we must better characterize the impact.

## Slide 50: Double Wheel Shooter
Two methods of launch:
Inelastic collision: Final surface speed of Launch wheels =

## Slide 51: Double Wheel Shooter
Two methods of launch:
Inelastic Collision:
Friction Drive:
Notes: Inelastic collision uses less energy

## Slide 52: Double Wheel Shooter
Inelastic Collision:
Friction consistency not as important; Final speeds must match.
Friction Drive:
Wheel speed accuracy not as important
Energy loss on wheels are larger
Notes: Friction Drive uses more energy; If friction force is the same, then launch wheel will travel a larger angle than the Inelastic collision.

## Slide 53: Double Wheel Shooter - Inelastic
Initial Momentum:
Wheel Momentum
Notes: Friction Drive uses more energy; If friction force is the same, then launch wheel will travel a larger angle than the Inelastic collision.

## Slide 54: Double Wheel Shooter - Inelastic
Momentum Conservation
Note: Shot distance will start falling when wheels start failing to match projectile speed.
Notes: If increasing wheel speed results in shorter shot, then wheels are not in contact at the end of the shot; Much like a skidding car.

## Slide 55: Single wheel launchers
Projectile rolls along one edge
If launch velocity is V,
...how fast does drive wheel need to turn?

## Slide 56: And Here’s the Math…
V
0
-V
Rotation Motion Only

## Slide 57
V + V = 2V
0 + V = V
-V + V = 0
Rotational and Translational Motion

## Slide 58: Momentum Transfer in Launcher

## Slide 59: Force to Accelerate in Distance
If we accelerate our projectile over a distance d, to reach a launch velocity V, how much constant force must applied to the projectile?
Our Example:
g=10m/s2; back of envelope calculation...

## Slide 60: Squeeze Force to Accelerate in Distance
If we must apply a force F to accelerate our projectile, how much force must we apply to the rim or surface of our projectile?
A high friction surface μ>1, can reduce the grip force

## Slide 61: Additional Topics
Time to Speed
Improving contact time (wheel shooter)
zero force on backing plate (single wheel shooter)

## Slide 62: Throwing Balls and other stuff
Understand the physics!
Separate the well known problems
  trajectories
  momentum and energy transfer
...from variants.
  inconsistent balls ( shape, weight, compliance...)
  inconsistent ball paths thru machine
  :
  and Build a Better Machine!

## Slide 63: Throwing Balls and other stuff
David Giandomenico December 13, 2014

## Slide 64: Specify the projectile trajectory
Need to know speed & spin requirements of the shooter
1) Specify the projectile’s trajectory (height, distance, entry angle etc.)
2) Compute launch velocity
3) Calculate energy requirements of projectile
Start shooter design:
1) Select a candidate design
2) Analyze momentum & energy to determine speeds
3) Consider grip forces on projectile
4) Parts selection ( e.g. wheel selection )
5) Gear-motor selection
Iterate
Scope of Talk

## Slide 65: Specify the projectile trajectory
Need to know speed & spin requirements of the shooter
1) Specify the projectile’s trajectory (height, distance, entry angle etc.)
2) Compute launch velocity
3) Calculate energy requirements of projectile
Start shooter design:
1) Select a candidate design for launcher
2) Analyze momentum & energy to determine speeds
3) Consider grip forces on projectile
4) Parts selection ( e.g. wheel selection )
5) Gear-motor selection
Iterate
Scope of Talk

## Slide 67: Angular Momentum
Moving momentum in our launch wheel to our projectile.

## Slide 68: Torque for a particle of mass m
Torque for a particle m
a more mathematically rigorous approach:
Notes: The more rigorous approach allows a general computation, without having to decompose the normal and in-line components of forces.

## Slide 69: System of particles
Now, let’s consider a system of particles...
...or a mass M of some shape:

## Slide 70: Moment of Inertia of a Disk
Integrate shells of 2πrh:
Substitute the mass (by inspection):

## Slide 71: Angular Momentum
following the same math as before

## Slide 72: Converting Angular to Linear Momentum

## Slide 73: Projectile Momentum