## Slide 1: Introduction to Robot Subsystems
Presented By:
Funky Monkeys, Team 846
Available online at lynbrookrobotics.com
Resources > Workshops > WRRF Workshops

## Slide 2: Choosing The Right Drivetrain
Presented by Eva Lomazov & Owen Li

## Slide 3: What is a Drivetrain?
Subsystem of the robot responsible for movement on the FIRST Competition Field
Includes:
  Motors
  Gearboxes
  Transmission
  Wheel Layout
Notes: Which consists of the motors that convert electrical energy into rotational motion, reduced to the right speed through gearboxes, and transferred through a chain or belt arrangement of some sort to the wheels that contact the ground to produce movement. This subsystem has to satisfy a certain set of requirements to be effective in FRC.

## Slide 4: Drivetrain Requirements
Common Features:
  Fast
  Turns Easily
  High Acceleration
FIRST Competition Demands:
  Turns in Place
  Pushes Hard
Notes: Now, let’s see a drivetrain design that does not meet these requirements . . .

## Slide 5: Ackerman Steering
Team 34’s Design on Chief Delphi
Notes: Distinction between common for frc and everyday. So . . . Let’s talk about what does work.

## Slide 6: Differential/Tank Steering
Power left and right sides independently
Features:
  Simple
  Easy to program
Team 846’s 2013 Drivetrain Design
Notes: Swap picture… comment that not only treads we have wheels same concept

## Slide 7: Four Wheels Differential Steering
Wheels slide to turn
Notes: Bt how well does this work???? Lets look at some math.

## Slide 8: Terminology:
µ = Coefficient of Friction
Weight = Weight of the robot
F = Force
T = Torque
Track (W )
Wheelbase
(L)
Notes: Coefficient of friction is the ratio between the force acting horizontally required to produce sliding and the normal force between the surfaces.
Force is an influence that causes an object to move.

## Slide 9: Ability to Turn
Wheels generate force while friction resists
  Ability to Turn =
  Turning Torque – Resisting Torque

## Slide 10: Maximum Tractive Force Per Wheel (FTMax)
Track (W )
Wheelbase (L)

## Slide 11: Max Turning Torque (TTMax)
Track (W )
Wheelbase
(L)
W/2
Notes: Loosely speaking, torque is a measure of the turning force on an object such as a bolt or a flywheel. For example, pushing or pulling the handle of a wrench connected to a nut or bolt produces a torque (turning force) that loosens or tightens the nut or bolt.
Max tractive force [maximum force exert on ground so it doesn’t slip] per wheel is coefficeint of friction (ratio of force needed to push it over the normal force object is inserting [weight] ) times total weight over number of wheels.
Maximum

## Slide 12: Maximum Resisting Torque (TResisting)
Track (W )
Wheelbase
(L)
L/2
Notes: Maximum force apply to wheel so it doesn’t move sideways.

## Slide 13: Turning Torque v. Resisting Torque

## Slide 14: 4 Wheel Layout
Remember: Turning Force – Resisting Force
  Only wide robots can turn
Team 846’s 2009 Drivetrain Design
Notes: What are the disadvantages of having a short wheelbase? How can you have the stability of a long wheelbase with the ability to turn of a short wheelbase?

## Slide 15: 2 Wheels, 2 Omniwheels
Omniwheels
  90° rollers allow sideways motion
Center of rotation between non-omni wheels
4 wheels provide tractive force
No Wheels Resist
c
c
c
c
c
c
Notes: Please view this slide as it will be animated during the presentation or slide the omniwheel over to see the text.

## Slide 16: 2 Wheels, 2 Omniwheels
Advantages
  No resisting torque
  Simple
Disadvantages
  Asymmetric
  Susceptible to defense
c
c
c
c
c
c
Notes: Please view this slide as it will be animated during the presentation or slide the omniwheel over to see the text.

## Slide 17: 6 Wheel Layout
Weight spread over 6 wheels
Only 4 wheels resist turning
Notes: View the slide with the animations.

## Slide 18: Turning Torque v. Resisting Torque

## Slide 19: Six Wheels Dropped Center
Center wheels dropped about 1/8 inch
  Theoretical Zero Resisting Torque
  Rocks on center when turning
30%
10%
10%
Team 846’s 2007 Robot
Notes: But now lets look at some other ways to make robots turn more easily

## Slide 20: Swerve Drive
Wheel modules rotate
Features:
  Sideways movement
  High traction wheels
Drawbacks:
  More complicated
  Higher Software Skill Required
  Heavy load on resources
    More parts to machine
    More gearboxes
Craig Hickman’s Design on Chief Delphi

## Slide 22: Mecanum Wheels
45° Rollers allow lateral movement

## Slide 23: How it works: Forward movement
http://wiki.robojackets.org/images/0/08/2007_TE_Session_-_Drive_Trains_(Handouts).pdf

## Slide 24: How it works: Sideways movement
http://wiki.robojackets.org/images/0/08/2007_TE_Session_-_Drive_Trains_(Handouts).pdf

## Slide 25: Mecanum Drive
Demo: http://www.youtube.com/watch?v=JGAlalbpBLA&feature=related
Features:
  Sideways movement
Drawbacks:
  Easy to Push
  Higher Software Skill Required
  Heavy load on resources
    More gearboxes
    Expensive wheels
Notes:   http://www.youtube.com/watch?v=JGAlalbpBLA&feature=related

## Slide 26: Conclusion
Exotic Drives
  Cool factor
  May give key advantage in a particular game.
Tank Drivetrain
  Simple solution - rugged & reliable
Notes: Irfanview

## Slide 27: Videos
Omni, Mecanum, Swerve drive examples
  http://www.youtube.com/watch?v=r5WKgQJtToM
Nona-drive (another exotic drive)
  http://www.youtube.com/watch?v=_hTyXQUgYLE&feature=related

## Slide 28: Electrical Subsystem
Presented by:
The Funky Monkeys Team 846
Alex Shmakov, Srinjoy Majumdar
Notes: Electrical = power distribution + power control
Electronics = low power sensors and circuits
BDCComm

## Slide 29: FIRST Power Distribution Diagram

## Slide 30: Power Distribution Diagram
Robot Controller
Notes: Make motor in the corner smaller to resemble scaling
Make CPU darker
Put red/black lines closer together
Put currents for the branches – CPU = 20 A, Spike = 20 A, Speed Controller = 40 A,

## Slide 31: Battery
12V Lead Acid Battery (18Ah)
13 Pounds
Provides over 100 amperes of current. Total output of over 1200 watts of power.
Can supply over 700 amperes of current when terminals are shorted.
Notes: Explain battery safety
Two hands because it is heavy
Nylon stop nut is a tip
Remove #10 screw - done
Smaller than a car battery
Fix spacing
Remove bullet point for take precautions
Change text
NEED TO SAY
Terminals are separate
Wrench
Welded together

## Slide 32: Robot Power Switch
Used to turn robot on and off, including emergency shut off
Also a 120 amp circuit breaker
Must be placed in an accessible location
Notes: Not located accessibly
Should be in an easy-to-access area
On/Off switch
Fire hazard
Retitle to robot power switch
120 amp circuit breaker
Control should be changed to limit
Exceed 120 amps and it will break
Remove bullet points when not necessary
High current switch
Handles high enough current
Primary importance
Doubles as a circuit breaker

## Slide 33
20-40 Ampere Fuse Location
Branch circuit power connection
Main Power Connection
Power Distribution Board
M6 Stop Nuts

## Slide 34
DC To DC Converters
Used to change voltage coming from battery to specific voltage required in branch circuit
  12V-5V
  12V-24V (for robot controller)

## Slide 35: Power Distribution Diagram
40A
20A
100A
18AWG
18AWG
12AWG
6AWG
Robot Controller
Notes: Make motor in the corner smaller to resemble scaling
Make CPU darker
Put red/black lines closer together
Put currents for the branches – CPU = 20 A, Spike = 20 A, Speed Controller = 40 A,

## Slide 36: American Wire Gauge
Wire thicknesses are based on the AWG (American Wire Gauge) System
  AWG wire thicknesses are based on number of wire draws – Higher gauge = thinner wire
Notes: Explain safety concerns when using smaller diameter wires

## Slide 37
American Gauge System
Undrawn Wire
Draw Plate 1
Draw Plate 2
Draw Plate 3
Gauge 1
Gauge 2
Notes: oAll wire from battery to PD have min #6 AWG (4.11mm) wire <R39 & Fig.4-8>
o40 amp breakers have min #12 AWG (2.052mm) wire <R44>
o30 amp breakers have min #14 AWG 1.628mm) wire <R44>
o20 amp breakers have min #18 AWG (1.024mm) wire <R44>

## Slide 38: Motors (FRC 2013)
Name | # in KOP | Total Allowed
CIM | 2 | 6
AndyMark 9015 | 2 | 4
Window Motors | 1 | 2
MiniCIM motor | 1 | 4
Automotive Window Motor
RS Series Motor
CCL Industrial Motors Limited (CIM)
MiniCIM motor
Notes: Replace with collection of motors
Only allowed to use motors inside the kit
Be aware that the rules may specify that you can buy extra motors (of the same type)
Discuss major types of motors
FIX:
scaling of pictures
Mabuchi is the motor on the left
Caption
Properly identify with companies
CIM = CCL industrial motor
Johnson electric motors for FP
Mabuchi

## Slide 39: Robot Controller CompactRIO National Instruments Embedded Controller
2013 cRIO; 4 Slots
  Software
    LabView, C++, Java
    vxWorks operating system.
    Field Programmable Gate Array (FPGA) provides real time data from the robot.
  Power
    24V Power via PD Board.
  Processor
    400 MHz Freescale MPC5125.
  Memory
    256MB System.
    512MB Storage.
The “Brain” of the robot Sends control signals to components
Notes: Servo testers at hobby stores to generate control signal for ESCs
Speaking
Servo is closed loop motor control
Expand ESC
Fix
CPU darkness

## Slide 40: PROBLEM!
The cRIO cannot directly control the motors.
  Cannot provide enough power
Solution:
  Motor Controllers
    Relays
    Electronic Speed Controllers

## Slide 41
cRIO
Motor Controller
Motor
Connections
Copper Wire

## Slide 42: Spike Relays
Relays close or open the circuit based on signals from the cRIO.
Contains two independently controlled SPDT* relays arranged in an H-Bridge
*SPDT = Single Pole Double Throw switch

## Slide 43: How an H-Bridge Works
MOTOR
+12V
Ground
S1
S3
S4
S2
S1+S4
FULL FORWARD
S3+S2
FULL REVERSE
S1+S3
BRAKE

## Slide 44: Electronic Speed Controller (ESC)
Control the amount of power sent to the motors in addition to direction that motor turns.
Three types of ESC’s:
Victor 888 ESC Jaguar ESC Talon ESC
Notes: 2004+ Victor
2009+ Jaguar

## Slide 45: Speed Controller Comparison
 | Victor ESC | Talon ESC | Jaguar ESC
Size | Small | Small | Large
Communication | Servo Wire | Servo Wire | Servo and CAN Bus
Price | $69.99 | $59.00 | $79.99
Notes: 2004+ Victor
2009+ Jaguar

## Slide 46: Pulse Width Modulation (PWM)
Pulse Width Modulation is used in two ways on our FIRST Robots:
  To provide a varying amount of power to the motors.
  To communicate with the Speed controller.

## Slide 47: Variable Power Delivery
The Speed Controller varies the power delivered to the motors by changing the “Duty Cycle.”
12V
0V
PERIOD (ms)
DUTY CYCLE (%) = TIME ON
PERIOD
12V
0V
DUTY CYCLE

## Slide 48: Speed Controller Communications using PWM
RC Model Aircraft standard:
The width of the pulse is measured as unit of time. Time which each pulse lasts is the pulse width.
Signal:
1.5 ms
±
0.5 ms
40 ms
(20ms-50ms)
2.0 ms = full forward
  1.75 ms = 50% fwd
1.5 ms = off
1.0 ms = full reverse
Notes: Voltage applied only 50% instead of power
Variable resistor first
On and off so no mechanical switch
Transistor
Introduce new slide for communication (see bottom of these notes)
Remove odd picture
Radio control signal for the Victor
Describe frame from 20ms to 40ms
PWM communication
Immune to electronic noise
Introduce slide for communication
Spike with three wires - 3 wire servo cable
Victor/Jag use PWM data signal + description
Jaguar also has data communication port for the CAN-Bus

## Slide 49: Speed Controller Communications
There are two ways to communicate with the Jaguar ESC
  Servo Wire
    Uses Pulse Width Modulation
  CAN-bus
    Uses “Message based protocol” (like Ethernet)

## Slide 50: CAN-Bus
“CAN” Stands for “Controller Area Network”
Is a single chain of point-to-point connections
The “bus” goes around the chain delivering the signal to different addresses – each ESC has its own address
2 CAN
ESC
ESC
cRIO
ESC
ESC
ESC
ESC
ESC
ESC

## Slide 51: How does the CAN-bus simplify wiring?
ESC
ESC
cRIO
ESC
ESC
ESC
ESC
ESC
ESC
2 CAN
ESC
ESC
cRIO
ESC
ESC
ESC
ESC
ESC
ESC
(Daisy Chaining)
Although the amount of wires is the same in each case, without the CAN-bus, the wires have to stretch all the way across the robot from the cRIO to each ESC, whereas with the CAN-bus, they are all linked together in a single chain.

## Slide 52: CAN-Bus Wiring
Telephone-style RJ11 instead of servo wire
Easy to make custom length with crimp tool
Can’t be put in backwards
Servo Wire
Telephone Wire
Notes: Called servo wire because it is used to connect to the servos of remote-controlled vehicles
NEED TO SAY
Servo wire coming loose
Crimper cheap at Radio Shack/Home Depot

## Slide 53: Power Distribution Diagram
Robot Controller
Notes: Make motor in the corner smaller to resemble scaling
Make CPU darker
Put red/black lines closer together
Put currents for the branches – CPU = 20 A, Spike = 20 A, Speed Controller = 40 A,

## Slide 54: Sensors and Electronics
Presented by:
Brent Yi
Raphael Chang
Manoj Vasishta
Notes: Manual vs Automation

## Slide 55: Why use sensors?
Increased performance
  Speed
  Preset Positions
Safety
  Prevent robot from damaging itself

## Slide 56: Sensors
Potentiometer
Encoder
Infrared Proximity
Limit Switch
Ultrasonic
Gyro
Hall Effect
Accelerometer
Camera
Kinect

## Slide 57: Limit switch
A simple switch
Can be set up to be triggered near a physical limit
$

## Slide 58: Hall effect sensor
Detects a magnetic field
Longer range
Can switch much faster than a mechanical switch
$

## Slide 59: Potentiometers (Pots)
Sensor for measuring position:
  Rotation, distance, etc.
$

## Slide 60: Potentiometers (Pots)
+5V
Ground/0V
5V
2.5V
0V
+5V
GND
Output
Simplest type:
Slider
Slider is connected to output.
10 KΩ
+5V
Ground/0V
100%
50%
0%

## Slide 61: Types of Potentiometers (pots)
Slide
Rotary

## Slide 62: Pots: Uses
Sense position: e.g. lift
How to sense the lift position?
  Travel length is 6 feet
  No linear pot long enough

## Slide 63: Multi-turn Pots
Multi-turn pot:
  Usually 3, 5, or 10 turns
  $$
Alignment is important!
  Continuous rotation: use encoder
Notes: Move pot picture

## Slide 64: Quadrature Optical Encoders

## Slide 65: Quadrature Optical Encoders
Determining Distance Travelled
  Count pulses
Determining Speed
  Count pulses over time period
  Measure time between pulses (faster and more accurate)
Notes: Do in one slide just say two different ways

## Slide 66: Quadrature Optical Encoders
Optical Sensor (A)
to controller
Optical Sensor (B)
to controller
A Channel
B Channel
Notes: Improve animation and show waveform
Angles?
More than one tick
Directions
Spin animation

## Slide 67: Quadrature Optical Encoders
Optical Sensor
to controller
Optical Sensor
to controller
Notes: Brush over
Just more ticks
Remove optical sensor

## Slide 68: Other Encoders
Our 2006 robot’s ball launcher
Hall Effect Sensor, and embedded magnet in wheel
Using encoder as a speed sensor
for fast-spinning wheels
Notes: Make your own encoders
Don’t need quadrature

## Slide 69: Sensing Distance: Ultrasonic Sensors
Determine distance
Send pulse of sound
Measure time until echo
Notes: CONS such as sensitivity to soft and irregular surfaces
Noisy environment may cause problems

## Slide 70: Infrared Proximity Sensors
Determines distance to object in front of it
Analog voltage reading
vs. ultrasound:
  Shorter range
  Faster
Notes: Sensing game pieces inside your robot
Short range non contact sensing

## Slide 71: Accelerometer
Detects gravity
Useful for tracking orientation
  3 axis accelerometer
Example: Driving Up Incline
Example: Balancing on Bridge

## Slide 72: Yaw Rate Sensor
Also commonly known as a gyro
Indicates rotational velocity
  Must take integral for angle
Prone to drift
  Calibrate before each use

## Slide 73: Camera
Senses field elements
  reflective targets, shapes, colors
Needs lots of processing power
  secondary computer may be required
Advanced programming
Time-consuming to use effectively
Notes: CAUTION

## Slide 74: Kinect Camera
RGB-D
With proper processing easier to make reliable
  Depth image not dependant on lighting
  Still not a magic bullet
All the pitfalls of regular camera
Notes: CAUTION

## Slide 75: Conclusion
Use sensors whenever possible
Sensors help make things safe
Benefits must overcome added complexity
Important part of a great robot

## Slide 76: Pneumatics
By Pransu and Akhil

## Slide 77: Pneumatics - Definition
Pneumatics is the use of pressurized air to achieve mechanical movement
Jack Hammer
Nail gun
Pneumatics?
Notes: Presenter: Akhil
Pneumatics is the use of pressurized air to achieve mechanical motion. Pneumatics is most commonly used in tools such as jack hammers, drills, and nail guns.

## Slide 78: Overview of Pneumatics System
Notes:     Presenter: Akhil
    compressor - generate pressure
    actuator - transform pressure to motion
    solenoid - controls the motion of actuator
    regulator – limits air flow to usable, steady flow rates
    tank – store air in
    tubings and fittings - let the air flow

## Slide 79: Compressor
Transducer of energy in pneumatic system
  Can Generate up to 120 PSI (Pounds per Square Inch)
Compacts air
Viair Compressor in FIRST Kit of Parts
Notes: Presenter: Pransu
The compressor provides the pneumatic system its energy by using the electrical energy from the battery to compress air.
This is the Compressor (Viair 090C air compressor) that FIRST provides to rookie teams.
Pump types:
positive displacement
  rotary
    lobe
    screw
    liquid ring
    scroll
    vane
  reciprocating
    diaphragm
    single acting
    double acting
dynamic
  centrifugal
  axial

## Slide 80: Diaphragm pump
Notes: Presenter: Nikunj
Typically, the compressor utilizes a diaphragm pump, in which the motor is powered by a battery and used to compress air in the enclosed space. The pressure gauge here indicates the pressure at the output of the compressor. When the pressure of the output has reached a certain limit, typically 120 psi, the electrical pressure switch here opens and turns of the compressor. Unfortunately, there are small leaks in the system that vent pressurized air. When the pressure switch detects that the pressure has dropped below a certain value, usually 115 psi, the electrical pressure switch closes and turns the compressor back on.

## Slide 81
From FIRST pneumatics manual
Notes: Presenter: Pransu
This energy from the compressed air gets converted into mechanical motion in the actuators

## Slide 82: Actuators
Actuators convert the difference in air pressure to mechanical motion
Linear actuators (also known as cylinders)
Narrower actuators move more quickly
Notes: Presenter: Pransu
(Demo)

## Slide 83
From FIRST pneumatics manual
Notes: Presenter: Akhil
Now that we see the basics behind pneumatics, we want to know how to usefully incorporate it into our robot when we’re designing it. To do this, we need to control several factors that affect the mechanics of actuators. The first factor is output pressure.

## Slide 84: Solenoid Valves
Controlled by the robot’s CPU
Solenoids opens a port to pressure when a voltage is applied
Double solenoids controls two ports
  When one port is open, the other is closed
Festo single solenoid valve
Festo double solenoid valve
Notes: Presenter: Akhil
You see how we controlled which way the cylinder moves with a click of a button. Often times we also want to control when we send compressed air to the cylinders or through which ports. For example, suppose you have a pneumatic pistons that you want to use a cylinder to lift something at the finale. We do this with electric solenoid valves. Although these valves are controlled electrically by the robot’s CPU, they can also be mechanically operated by pressing these buttons. A single solenoid valve allows you to open one port of a cylinder to pressure when voltage is applied, or when I press this button, causing the cylinder to either extend or retract. When voltage is no longer applied, the valve releases the pressure to atmosphere, and whatever load is on the piston will cause it to return to its original position.
Orig load: spring, gravity
A double solenoid valve allows you to use the cylinder in both directions. When I press this button or when voltage is applied to this solenoid, the valve would open the blue side to atmosphere and the white side to pressurized air, causing the cylinder have an extending force. When the other solenoid is activated, the white side is open to atmosphere and the blue side to pressurized air, causing the cylinder to have a retracting force.
(Demo)

## Slide 85
From FIRST pneumatics manual
Notes: Presenter: Pransu
(Demo)
But as we can see, there is a problem with this system; the actuator is moving slower and slower. This is because the compressor is forced to constantly compress air in order to move the piston in the actuator but is unable to meet such demands. In order to resolve this issue, we need a method of storing compressed air until it is needed; thus, we need a tank!
\

## Slide 86: Tank
Tanks are a reserve of compressed air
Maximum of 120 psi for First competitions
Notes: Presenter: Pransu
Plastic vs. Metal = weight concern
How many movements can we do with one tank?
(Demo)

## Slide 87
From FIRST pneumatics manual
Notes: Presenter: Akhil
Now, suppose we want 60 psi of pressure but we know that the pressurized air from the compressor is outputting much more than that. So, how would we limit the air flow to the desired amount? By adding a regulator!
Now that we see the basics behind pneumatics, we want to know how to usefully incorporate it into our robot when we’re designing it. To do this, we need to control several factors that affect the mechanics of actuators. The first factor is output pressure.

## Slide 88: Regulator
Maintains a constant level of pressure.
  Working air pressure
Maximum of 60 psi for FIRST competitions
Notes: Presenter: Akhil
The regulator limits and maintains a constant level of pressure. You can see here that the pressure at the output of the compressor is at 120 psi, but FIRST only allows us to operate our actuators at a maximum of 60 psi. We achieve this pressure drop by using a regulator. It drops the input pressure to an output pressure that you can set by turning this knob. This gauge above the regulator shows pressure that being outputted.

## Slide 89
From FIRST pneumatics manual

## Slide 90: Common Valves and Fittings
Pressure switch
Pressure relief valve
Plug valve
Flow-rate valve
Notes: Presenter: Pransu
Notice this cylinder. On this end it has a common L join, but the one on this side has a screw on top. This is a flow-rate valve. <explanation> Because of this, you can fit two of these valves on the cylinder and that allows you to independently control the extending and retracting speeds.

## Slide 91: Inside Pneumatic Actuator
Notes: Presenter: Akhil

## Slide 92: Finding Linear Force (Extending)
92
Notes: Presenter: Akhil

## Slide 93: Example Calculation
0.75 in
= =0.44sq-in
Force = 40 psi X 0.44 sq-in = 17.6 lbs
17.6 lbs
40 psi
Notes: Presenter: Akhil

## Slide 94: Forces of Different Bore(Diameter) Cylinders at 40 psi and 60 psi
From FIRST pneumatics manual
Bore (inches) |  | 0.75 | 1.50 | 2.00
40 psi | Extending | 18 lbf | 71 lbf | 126 lbf
 | Retracting | 16 lbf | 65 lbf | 113 lbf
60 psi | Extending | 26 lbf | 106 lbf | 188 lbf
 | Retracting | 24 lbf | 97 lbf | 170 lbf
Notes: Presenter: Akhil
Wasn’t doing all that math fun!? Well here is a table with basic numbers so you don’t need to do all that math again.

## Slide 95: Finding Retracting Force
95
D
Notes: Presenter: Akgil

## Slide 96: Overview of Pneumatics System
Notes:     Presenter: Pransu

## Slide 97: Introduction to Robot Subsystems
Presented By:
Funky Monkeys, Team 846
Available online at lynbrookrobotics.com
Resources > Workshops > WRRF Workshops