## Slide 1: Electrical subsystem
Notes: Manual vs Automation

## Slide 2: Power Distribution Diagram
Notes: Make motor in the corner smaller to resemble scaling
Make CPU darker
Put red/black lines closer together
Put currents for the branches – CPU = 20 A, Spike = 20 A, Speed Controller = 40 A,

## Slide 3: FIRST Power Distribution Diagram

## Slide 4: Battery
Voltage: 12 Volts Nominal​ Weight: 13 Pound​ Chemistry: Lead-Acid (Gel)​ Capacity: 18 Ah​ 10.2 Ah when rated for 1 hour​
​
Current: Nominal 150 A​ Power: ~1600 Watts at 150 A​ ​
Can supply over 700 amperes of current when terminals are shorted.
Notes: Explain battery safety
Two hands because it is heavy
Nylon stop nut is a tip
Remove #10 screw - done
Smaller than a car battery
Fix spacing
Remove bullet point for take precautions
Change text
NEED TO SAY
Terminals are separate
Wrench
Welded together

## Slide 5: Robot Power Switch
Used to turn robot on and off, including emergency shut off
Also a 120 amp circuit breaker
Must be placed in an accessible location
Notes: Not located accessibly
Should be in an easy-to-access area
On/Off switch
Fire hazard
Retitle to robot power switch
120 amp circuit breaker
Control should be changed to limit
Exceed 120 amps and it will break
Remove bullet points when not necessary
High current switch
Handles high enough current
Primary importance
Doubles as a circuit breaker

## Slide 9: Power Distribution Diagram
40A
20A
100A
18AWG
18AWG
12AWG
6AWG
Notes: Make motor in the corner smaller to resemble scaling
Make CPU darker
Put red/black lines closer together
Put currents for the branches – CPU = 20 A, Spike = 20 A, Speed Controller = 40 A,

## Slide 10: American Wire Gauge
Wire thicknesses are based on the AWG (American Wire Gauge) System
  AWG wire thicknesses are based on number of wire draws: Higher gauge = thinner wire
Notes: Explain safety concerns when using smaller diameter wires

## Slide 11: American Gauge System
Undrawn Wire
Draw Plate 1
Draw Plate 2
Draw Plate 3
Gauge 1
Gauge 2
Notes: oAll wire from battery to PD have min #6 AWG (4.11mm) wire <R39 & Fig.4-8>
o40 amp breakers have min #12 AWG (2.052mm) wire <R44>
o30 amp breakers have min #14 AWG 1.628mm) wire <R44>
o20 amp breakers have min #18 AWG (1.024mm) wire <R44>

## Slide 12: RoboRIO

## Slide 13: RoboRIO
2014 RoboRIO
  Power
    6.8-16V via PDP
  Processor
    Dual-Core ARM Cortex™-A9 at 667 MHz .
  Memory
    256MB System.
    256MB Storage.
  PWM
    10 Ports
  USB
    2 USB Host and

## Slide 14: Problem!
The roboRIO cannot directly control the motors.
  Cannot provide enough power
Solution:
  Motor Controllers
    Relays
    Electronic Speed Controllers

## Slide 15: Connections
roboRIO
Motor Controller
Motor
Copper Wire

## Slide 16: Spike Relays
Relays close or open the circuit based on signals from the cRIO.
Contains two independently controlled SPDT* relays arranged in an H-Bridge
*SPDT = Single Pole Double Throw switch

## Slide 17: How an H-Bridge Works `
MOTOR
+12V
Ground
S1
S3
S4
S2
S1+S4
FULL FORWARD
S3+S2
FULL REVERSE
S1+S3
BRAKE

## Slide 18: Electronic Speed Controller (ESC)
Control the amount of power sent to the motors in addition to direction that motor turns.
Two types of ESC’s:
  Talon SRX
  Victor SP
Notes: 2004+ Victor
2009+ Jaguar

## Slide 19: Comparison
Talon SRX | Victor SP
$79.99 | $59.99
Features | Similar Features | Features
CAN & PWM communication 6-28V | Small & light Embedded power and output Completely Sealed 12V Nominal | PWM communication 6-16V

## Slide 20: Size Comparison

## Slide 21: Speed Controller Communications
There are two ways to communicate with the Jaguar ESC
  Servo Wire
    Uses Pulse Width Modulation
  CAN-bus
    Uses “Message based protocol” (like Ethernet)

## Slide 22: Difference between CAN and PWM Wiring
ESC
ESC
roboRIO
ESC
ESC
ESC
ESC
ESC
ESC
ESC
ESC
cRIO
ESC
ESC
ESC
ESC
ESC
ESC
(Daisy Chaining)